AM2320
Temperature and humidity combined sensor AM2320 digital temperature and humidity sensor is adigital signal output has been calibrated.

Pin	Name	Description
1	VDD	Power Supply
2	SDA	Serial data, bidirectional port
3	GND	Ground
4	SCL	Serial Clock Input Port (Single Bus Ground)

Electrical Characteristic
Parameter	Condition	Min	Typ	Max	Unit
Supply Voltage		3.1	5	5.5	v
Power Consumption	Dormancy	8	10		µA
	Measure		950		µA
	Average		350		µA
Low-level output voltage	ICC5	0		300	MV
High-level output voltage	Rp<25 kΩ	90%		100%	VDD
Low-level output voltage		0		30%	VDD
High-level output voltage		70%		100%	VDD
Rpu6	VDD = 5V / VIN = VSS	30	45	60	kΩ
Output Current			8		MA
		10	20		µA
Sampling Period			2.0		s

Relative Humidity Characteristic
Parameter	Condition	Min	Typ	Max	Unit
Resolution			0.1		%RH
Range		0		99.9	%RH
Accuracy	25°C		±3		%RH
Repeatability			±0.1		%RH
Interchangeability		Completely interchangeable
Response Time	1/e(63%)		<5		S
Sluggish			±0.3		%RH
Drift	Typical Values		<0.5		%RH/yr

Temperature Characteristic
Parameter	Condition	Min	Typ	Max	Unit
Resolution			0.1		°C
			16		bit
Accuracy			±0.5		°C
Range		-40		80	°C
Repeatability			±0.2		°C
Interchangeability
Response Time	1/e(63%)		<5		S
Drift			±0.1		°C/yr